## Slide 1: AIR LOCALIZE 1.1
2D – 3D
Spot Detection & Quantification
Timothee Lionnet, Singer Lab
timothee.lionnet@einstein.yu.edu

## Slide 3: Requirements
Runs only on Windows XP
1) Install MATLAB Compiler Runtime (run MCRInstaller.exe)
2) Open the windows command window (start menu > Run…> cmd)
3) Go to the directory where the AIRLOCALIZE1_1.exe is stored
4) Type AIRLOCALIZE1_1.exe

## Slide 4: Single z-stack Analysis: User Input
Chose Input mode
Load file
Select ROI (optional)
Compute PSF settings manually (optional)
Chose Threshold manually (optional)

## Slide 5
1) Chose input mode:
2) Load your File:

## Slide 6: Detection & Quantification Parameters
The width of the PSF resp. laterally and vertically (in pixel units).
If you do not know these,
check “Set Manually”
Check Yes if you only want to analyze a portion of the image (saves computation time)
Threshold Value that sets the detection sensitivity.
You can set it visually if you check “Set Manually”.
Chosing ‘Intensity S.D. ‘ Units can be useful when anayzing a times series with considerable bleaching.
Otherwise use ‘Absolute’
Where your results will be saved
You can safely ignore the Advanced Parameters

## Slide 7: Select a rectangular ROI
Navigate your z-stack with this scroll bar
A first click determines the position of the first corner. The second click determines the position of the opposite corner.

## Slide 8: Determine the PSF width (1)
You can change the contrast of the display in this panel
Mouse x,y position & corresponding Intensity
Navigate your z-stack with this scroll bar
Number of the displayed slice
Zoom Window centered on the current mouse position;
You can change the window size
Intensity profile of lines around the current mouse position (marked by the green vertical line). You can change the range of the graphs
Readout of the snap / grab mode status (see next)
Gaussian Fitting Commands (see next)

## Slide 9: Determine the PSF width (2)
Bring your mouse on top of a spot (avoid blobs).
2) Left-click to enter snap mode (the displays of the right panel should not refresh anymore when the mouse moves and the status readout should read snap).
3) Click on the “local gaussian fit” button.
4) Within seconds, the results should appear, and the fitted curve should overlay in red the intensity profiles in the x,y,z displays.
5) If the fit result is correct, click on the “Record Fit Results” button.
6) Left-click to return to grab mode (the displays of the right panel should now refresh when the mouse moves and the status readout should read grab).
Repeat for a few spots (~10) to determine the average PSF width.
The number of fits recorded should increase each time.
Push the “done” button (Make sure you have at least one fit recorded)

## Slide 10: Determine the threshold manually
Toggle the overlay that shows the predected spots to compare raw data with the thresholded spots
Change the threshold value here
Choice of Units: Intensity SD (useful on a timeserie with photobleaching)
Or Absolute
You can change the contrast of the green channel in this panel
Green: raw data
Red: spot candidates
Adjust the threshold value and check
visually
which spots are selected

## Slide 11
You then should be able to monitor the progress of the spot fitting in the command window.

## Slide 12: Automated saving
Saves in your selected directory 2 files:
The .loc3 file is a text file that contains the array with position, Intensity and frame number
The .par3 file is a text file that contains the parameters
The .det file is a matlab file containing both the results and parameters
Note that (x,y) coordinates are inverted from the Image J conventions.
The basename of each file is that of the original image (except for movies).

## Slide 13: Advanced parameters
Used to output
the final_spots
array
in physical units
rather than pixels
The size
of the
local ROI around each spot
on which the fit
is performed
(units of the
PSF width)
Thickness
of the pixel set
used to define
the
background
around the
local ROI
(local background)
Type of background
correction:
Global on the image
linear fit around
the ROI
Median of the pixels
surronding the ROI
In the smoothing filter,
sets the value of
the lower cutoff
Frequency
Minimum distance
allowed between
predected spots
Maximum number of spots to be quantified
(if more spots are predetected,
keeps only the brightest ones)
Maximum number allowed for the iterations
of the gaussian mask routine
Type of method used.
Gaussian mask is the most robust.

## Slide 14: Credits
Gaussian Mask Algorithm: Dan Larson
Tiff reader: Nedelec Lab
ROI selection: Andriy Nych